## Slide 1
Shamkya Mining Project
Integrating geology, geochemical pathfinder analysis, and Python-based visualization to support early-stage exploration decisions in orogenic gold systems.
By:
Obay Salih &
Salih Adam

## Slide 2
The Exploration Challenge
Nugget Effect Problem
Extreme grade variability over short distances makes gold distribution highly irregular in orogenic systems.
Pathfinder Strategy
Focus on associated elements and geochemical ratios to reduce uncertainty and identify core mineralized zones.
Spatial Analysis
Multi-element vectoring tools help distinguish proximal high-grade zones from distal background geochemistry.

## Slide 3
Data Sources and Integration
Sample Collection
ALS assay results from multiple sample types:
Diamond drill core
Reverse circulation (RC) chips
Trench and channel samples
Grab samples from surface exposures
Final Dataset
1,754 samples after cleaning and merging with complete spatial coordinates and geochemical data.
Key elements: Au, As, Sb, Bi, Zn, Ag, Cu
This forms the foundation for geochemical analysis, statistical modeling, and 3D visualization.

## Slide 4
Gold Distribution Characteristics
Strong Positive Skew
Histogram reveals numerous low-grade samples with a few extremely high-grade outliers.
Spatial Clustering
2D contour maps and 3D surface models visualize concentrated high-gold zones within the project area.
High-Grade Shoots
Distribution pattern supports localized structural controls creating discrete mineralized shoots.
The spatial distribution of gold shows distinct clustering in the central-eastern portion of the property, consistent with structurally-controlled orogenic gold mineralization.

## Slide 8
Pathfinder Element Correlations
1
Antimony (Sb)
Strongest positive correlation with gold. Key proximal pathfinder element in orogenic systems.
2
Silver (Ag)
Moderate positive correlation. Associates with gold-bearing sulfide assemblages.
3
Arsenic (As)
Positive but weaker than Sb. Common in broader mineralized halos.
4
Zinc (Zn)
Negative correlation. Represents distal zones away from gold concentration.
These correlation patterns match classical orogenic gold system geochemistry, validating the pathfinder approach for this deposit type.

## Slide 9
Geochemical Ratio Analysis
Sb/As Ratio
Emerges as the strongest vectoring tool. Higher ratios systematically occur closer to high-gold zones, providing a gradient toward mineralization.
Cu/Zn Ratio
Secondary indicator. Useful for distinguishing proximal copper-enriched zones from distal zinc-dominant background.
Scatterplot analysis confirms strong spatial correlation between elevated Sb/As and gold grade across the entire dataset.

## Slide 11
Geochemical Clustering Results
33%
Cluster A
Core mineralized zone — high gold, high Sb/As, elevated Ag
42%
Cluster B
Transitional halo — moderate pathfinder signals, intermediate gold
25%
Cluster C
Distal background — Zn-rich, low gold, low Sb/As
K-means clustering on multi-element geochemistry identifies three distinct geochemical domains that reinforce the zonation model from core to periphery.

## Slide 12
3D Pathfinder Index Modeling
A conceptual As–Sb–Hg pathfinder index demonstrates multi-element signal behavior in 3D space, even without Hg assay data.
01
Index Construction
Weighted combination of normalized pathfinder element values creates composite signal.
02
Spatial Visualization
3D surface interpolation reveals vertical and lateral extent of mineralized envelope.
03
Gold Correlation
High index values systematically coincide with gold hotspots, validating the approach.

## Slide 14
Geological Model Integration
Lithological Framework
Mineralization hosted primarily in granitic gneiss and sheared amphibolite units.
Structural Controls
High-grade zones align with regional-scale shear corridors and secondary splays. Structural dilation zones create fluid pathways.
Geochemical Validation
Sb/As ratios and cluster zoning patterns support structurally controlled core with outward geochemical gradients.
Deposit Classification: Orogenic gold system with characteristic pathfinder element associations and structural-lithological controls.

## Slide 15
Key Findings and Exploration Impact
Pathfinder Success
Sb/As ratios effectively reduce exploration uncertainty and vector toward high-gold zones.
Spatial Correlation
High-gold zones cluster in central-eastern project area with strong geochemical signatures.
Zonation Model
Three-cluster geochemical model from core to periphery guides drill targeting.
This integrated approach demonstrates that combining Python-based geostatistics with multi-element pathfinder analysis significantly improves targeting efficiency in orogenic gold exploration, reducing reliance on direct gold assays alone.

## Slide 16
Slide 10 — Final Interpretation
This project successfully demonstrates that pathfinder elements and ratios significantly reduce uncertainty in gold exploration. Specifically, strong correlations have been identified between high-gold zones and Sb/As ratios, with these promising areas spatially clustered within the central-eastern part of the project.

## Slide 17
Slide 11 — Impact & Value
Informed Drilling Decisions
The workflow provides data-driven insights, leading to more precise and effective drilling targets.
Improved Geological Understanding
Enhances comprehension of the orogenic gold system, revealing nuanced geological controls on mineralization.
Cost-Efficient Solutions
Utilizes open-source tools, significantly reducing reliance on expensive proprietary software in early exploration stages.
Reproducible Geochemical Model
Establishes a robust and repeatable geochemical model for ongoing and future exploration projects.

## Slide 18
Thank You
We appreciate your time and consideration of the Shamkya Mining Project. We look forward to exploring these promising opportunities further.